Clutch Adjustment

On Kz650’s the clutch should be adjusted every 3,100 miles or every oil change.  This will increase clutch life as well as making shifting easier.

First, in the middle of a clutch cable is an adjuster, loosen the lock nut and screw it both parts of the adjuster together giving the cable the most amount of slack.

Also loosen the locknut by the clutch lever so the adjusting barrel can turn freely and adjust the barrel so there is about 5-6mm between the adjuster and locknut.

Now move down to the cover where the clutch cable ends.  Remove the two screws holding in the adjusting cover.  Loosen the lock nut and back the screw out two turns or until it moves freely.

Screw it back in until it is hard to turn and then back it off approximately ½ turn and then retighten the lock nut being sure not to turn the adjusting screw.

Now go back up to the adjuster in the middle of the cable and unscrew it until all the slack has been taken out of the cable and the clutch lever does not have any free play and then tighten the locknut on it.

Back by the clutch lever adjust the barrel until there is about 3mm of slack between the cable end of the lever and the mount and then retighten the locknut.